## Slide 1: Lecture 1
Gromacs – input/output files and general operation
Michael Holmboe
Umeå University, Sweden

## Slide 2: Overview of this lecture
  What is Gromacs? Where do we find it, and how can we find some documentation? Any other programs we should know about?
  How do we typically run Gromacs?
  What are the input/output files of Gromacs?
  Example: Simulation of a small water box - How to setup a general simulation using different ‘workflows’ - Let’s look at some output

## Slide 3: 1/4 Gromacs?

## Slide 4: Gromacs (GROningen MAchine for Chemical Simulations)
  A molecular dynamics package mainly designed for simulations of proteins, lipids and nucleic acids. It was originally developed in the Biophysical Chemistry department of University of Groningen, and is now maintained by contributors in universities and research centers worldwide, mainly at the SciLife lab in Stockholm, Sweden.
Current development in the Gromacs and MD community
Using GPU ‘s
Copernicus - distributed computing and automatization…

## Slide 5: Software to install…
  Gromacs – use recent versions! Prior Gromacs-2016.x, there was version 5.1.x, 4.6.x, 3.x… See http://manual.gromacs.org/documentation/ for docs and download
  For data analysis (suggestions…)
  Xmgrace - recommended program for data handling/plotting .xvg data files. Download from http://plasma-gate.weizmann.ac.il/Grace/
  VMD 1.9.3 - Trajectory viewer, movie maker, analysis and more with different plugins. Register/download at http://www.ks.uiuc.edu/Research/vmd/
  Python - (2.7.x mostly used). Many third-party tools to Gromacs exist for Python
  Matlab - good for data handling/plotting (any recent version will do). Commercial but available at many Universities
  Free alternatives to Matlab: Octave/Scilab/Freemat
  Other software
  You need a good text editor. I use Textwrangler for MacOS, Vim in the bash shell.
  Avogadro 1.2 - molecular editor which I like. Do not use the most recent version, use 1.2. http://avogadro.cc/wiki/Main_Page
  Openbabel - can be pretty handy for file conversion
  Marvinsketch - is nice for drawing organic molecules
  ChemDoodle - is also nice for drawing organic molecules

## Slide 6: The documentation…
  See http://manual.gromacs.org/documentation/ for recent manuals, or http://manual.gromacs.org/documentation/2016.2/user-guide/index.htmlfor first time users.
  Also, http://manual.gromacs.org/online.html is a good starting point, or the http://manual.gromacs.org/programs/bytopic.html for all the utility and analysis programs and for the MD simulations settings: http://manual.gromacs.org/online/mdp_opt.html
  See also the old website http://www.gromacs.org It contains a lot of tips & tricks, although some stuff is outdated nowadays since the release of Gromacs 5.x
  Check out Justin Lemkul’s nice tutorials
  http://www.bevanlab.biochem.vt.edu/Pages/Personal/justin/gmx-tutorials/
  Also ,check out the mailing list for specific problems, just google [gmx-users] yoursearchterm (otherwise… just google)

## Slide 7: About the Gromacs documentation… Look for the most recent documentation…
www.gromacs.org
http://manual.gromacs.org/documentation/2016.3/index.html

## Slide 8: 2/4 How do we typically run Gromacs?

## Slide 9: 4 typical stages of running Gromacs
Constructing an input structure  .gro or .pdb file
Setting up the input files
 System topology, molecular topology, simulation settings…
Running the simulation (in parallell)
gmx grompp and gmx mdrun(_mpi)
Analyzing the trajectory/ thermodynamic data
Many ways to do this… manually or using VMD, Avogadro, Python, Matlab
Manually (for small molecules) or using some sort topology utility…
On local computer or HPC cluster in parallell
Analyzing the data with any of the many Gromacs utilities or Python, Matlab, Xmgrace or other tools

## Slide 10
http://manual.gromacs.org/online/flow.html
Generic flow chart of Gromacs simulations Does it always work?
  ‘Gromacs is a molecular dynamics package mainly designed for simulations of proteins, lipids and nucleic acids.’

## Slide 11: The general workflow for a MD simulation
Energy minimization simulation (EM)
Position restraints simulation (NVT)
Volume optimization simulation (NPT)
Production simulation/s (NVT or NPT or NVE)
Some initial structure/configuration from a .gro or .pdb file
em.gro/prenvt.gro
md.gro
nvt.gro/prenpt.gro
npt.gro/premd.gro
Relax the structures in the system, minimizing molecular overlap
Quick eq. run to allow for water re-orientation w. solutes
Density optimisation of the system, adjusting the volume
Gather statistics and data…

## Slide 12: How-to run Gromacs?
  GROMACS consists of ~90 different large or small programs/codes/utilities and relies on the UNIX command-line option philosophy. Adding “-h” gives you help for any command
Terminal commands to run Gromacs calling gmx mdrun (the actual simulation engine):
gmx mdrun # If using the default file names, we need no flags
gmx mdrun –f topol.tpr # with the –f flag
gmx mdrun –v –deffnm md # md is the common filename for all input/output files
gmx mdrun -deffnm md -cpi md # will do restart from previous md.cpt checkpoint file
gmx mdrun –multidir … # will start many parallell simulations simultaneously
Example on a HPC cluster (supercomputer)… more complicated but consult your local HPC center
srun -n 32 mdrun_mpi_sp –f md.tpr –tunepme
srun -n 32 mdrun_mpi_sp –f md.tpr –ntmpi 32 –ntomp 1 –tunepme # use -tunepme or –npme 8 or 12
srun -n 32 mdrun_mpi_sp –f md.tpr –ntmpi 16 –ntomp 2 –tunepme
srun -n 32 mdrun_mpi_sp –f md.tpr –ntmpi 8 –ntomp 4 –tunepme
Example of tuning mdrun on a HPC cluster with tune_pme and then launching mdrun with the best settings
export MDRUN='mdrun_mpi_sp'
export MPIRUN='srun'
gmx_sp tune_pme -v -mdrun "$MDRUN" -np 64 -npstring n -dlb yes -s md.tpr -check -launch -deffnm md \
-steps 15000 -resetstep 5000 -npme subset -ntpr 4 -rmax 1.4 -rmin 0.9 -r 1 -p -bg -err

## Slide 13: 3/4 Gromacs – input/output files and general operation

## Slide 14: What input files do we need to run Gromacs?
grompp.mdp (a MD parameter file)
topol.top (the system topology file)
#include ”spc.itp” ; molecule topology file
index.ndx (optional index file)
conf.gro (a structure file)
#include ”ffbonded.itp” ; ff file with bond parameters
#include ”ffnonbonded.itp” ; ff file with non-bonded parameters
topol.tpr is binary (but portable) and the only run input file needed for gmx mdrun
#include ”posres.itp” ; optional position restraints file
#include ”forcefield.itp” ; ff declaration file
Text input files needed for Gromacs pre-processor gmx grompp
(grompp == gromacs preprocesor)
gmx grompp –p topol.top –f grompp.mdp –c conf.gro –n index.ndx –o topol.tpr
To run Gromacs:
gmx mdrun –f topol.tpr # or something.tpr

## Slide 15: Gromacs input/output files
  Topology file/s (.top or .itp, sort of flexible format) Typically the molecular topology file is generated by the program gmx pdb2gmx. gmx pdb2gmx translates a pdb structure file of any peptide or protein to a molecular topology file. Hence we usually need something else than pdb2gmx to simulate an inorganic system.
  Molecular structure file (.gro, .pdb, sort of fixed format) First the program gmx editconf should be used to define a box of appropriate size around the molecule. gmx solvate solvates a solute molecule into any solvent (in this case water). The output of gmx solvate is a gromos structure file solvated in water.
  Molecular dynamics parameter file (.mdp, sort of flexible format)) The Molecular Dynamics Parameter (.mdp) file contains all information about the Molecular Dynamics simulation itself e.g. time-step, number of steps, temperature, pressure etc. The easiest way of handling such a file is by adapting a sample .mdp file. A sample mdp file can be found online.

## Slide 16: Gromacs input/output files
  Index file (.ndx, sort of fixed format) Sometimes you may need an index file to specify actions on groups of atoms (e.g. Temperature coupling, accelerations, freezing). Usually the default index groups will be sufficient, so for this demo we will not consider the use of index files.
  Run input file (.tpr, binary, use gmx dump or gmx check) The next step is to combine the molecular structure (.gro file), topology (.top file) MD-parameters (.mdp file) and (optionally) the index file (ndx) to generate a run input file (.tpr extension). This file contains all information needed to start a simulation with GROMACS. The gmx grompp program processes all input files and generates the run input .tpr file.
  Trajectory file/s (.trr .xtc .tng, binary, use gmx dump or gmx check) Once the run input file is available, we can start the simulation. The program which starts the simulation is called gmx mdrun. The only input file of gmx mdrun you usually need to start a run is the run input file (.tpr file). The output files of gmx mdrun are the trajectory file (.trr or .trj or .tng) and a logfile (.log file).

## Slide 17: Gromacs input/output files
  Parameter files
  .mdp - run parameters, input for gmx grompp and gmx convert-tpr
  Generic structure formats:
  .gro - the Gromacs format (tpr and cpt files also contain structural data)
  .pdb - brookhaven Protein DataBank format
  .pqr - pdb-like version, also contains charge (what precision?) and vdw radii
  .xyz - simple structure format, deprecated?
  Topology files
  .top - system topology (ascii)
  .itp - #include topology (ascii)
  .rtp - residue topology (ascii)
  .ndx - index file

## Slide 18: Gromacs input/output files
  Generic run Input files
  .tpr - system topology, parameters, coordinates and velocities (binary, portable)
  .tpa - system topology, parameters, coordinates and velocities (ascii)
  Structure+mass(db):
  .tpr, .tpb, .tpa, .gro or .pdb
  Structure and mass input for analysis tools. When gro or pdb is used approximate masses will be guessed..
  Generic trajectory formats:
  .tng - New format!!! Any kind of data (compressed, portable, any precision)
  .trj - x, v and f (binary, full precision)
  .trr - x, v and f (binary, full precision, portable)
  .xtc - x only (compressed, portable, any precision)
  .gro - x and v (ascii, any precision)
  .pdb - x only (ascii, reduced precision)

## Slide 19: Gromacs input/output files
  Generic energy formats:
  .ene - energies, temperature, pressure, box size, density and virials (binary)
  .edr - energies, temperature, pressure, box size, density and virials (binary, portable)
  Other files:
  .dat - generic, preferred for input
  .edi - essential dynamics constraints input for gmx mdrun
  .edo - essential dynamics constraints output for gmx mdrun
  .eps - encapsulated Postscript
  .log - log file
  .map - colormap input for gmx do_dssp
  .mtx - binary matrix data
  .out - generic, preferred for output
  .tex - LaTeX input
  .xpm - ascii matrix data, use gmx xpm2ps to convert to eps
  .xvg - xvgr input, to be used with xmgrace, can also easily be imported into Python, Matlab

## Slide 20
  How to setup the molecular topology for Gromacs
  i.e. the molecular topology file (.top or .itp, sort of flexible format)
  Gromacs comes with its own topology tool (gmx pdb2gmx) designed for proteins and some lipids
  gmx pdb2gmx -f someprotein.pdb –o processed.gro -water spce
  Select the Force Field:
  From '/usr/local/gromacs/share/gromacs/top':
  1: AMBER03 protein, nucleic AMBER94 (Duan et al., J. Comp. Chem. 24, 1999-2012, 2003)
  2: AMBER94 force field (Cornell et al., JACS 117, 5179-5197, 1995)
  3: AMBER96 protein, nucleic AMBER94 (Kollman et al., Acc. Chem. Res. 29, 461-469, 1996)
  4: AMBER99 protein, nucleic AMBER94 (Wang et al., J. Comp. Chem. 21, 1049-1074, 2000)
  5: AMBER99SB protein, nucleic AMBER94 (Hornak et al., Proteins 65, 712-725, 2006)
  6: AMBER99SB-ILDN protein, nucleic AMBER94 (Lindorff-Larsen et al., Proteins 78, 1950-58, 7: AMBERGS force field (Garcia & Sanbonmatsu, PNAS 99, 2782-2787, 2002)
  8: CHARMM27 all-atom force field (CHARM22 plus CMAP for proteins)
  9: GROMOS96 43a1 force field
  10: GROMOS96 43a2 force field (improved alkane dihedrals)
  11: GROMOS96 45a3 force field (Schuler JCC 2001 22 1205)
  12: GROMOS96 53a5 force field (JCC 2004 vol 25 pag 1656)
  13: GROMOS96 53a6 force field (JCC 2004 vol 25 pag 1656)
  14: GROMOS96 54a7 force field (Eur. Biophys. J. (2011), 40,, 843-856, DOI: 10.1007/ 15: OPLS-AA/L all-atom force field (2001 aminoacid dihedrals)
  Obviously do not work for other forcefields…

## Slide 21
  How to setup the molecular topology for Gromacs
  i.e. the molecular topology file (.top or .itp, sort of flexible format)
Some gromacs topology tools/scripts for organic molecules and forcefields
Use Gromacs gmx pdb2gmx if it works for you, or try gmx x2top –h If else have a look at these tools:
  AMBER Antechamber - Assigns the GAFF force field to the molecule
  ACPYPE - A Python interface to Antechamber, also OPLS/aa?
  CHARMM CharmmCGenFF, generalized force field for CHARMM
  SwissParam
  CHARMM-GUI, online server that works well in many cases
  GROMOS/UA PRODRG 2.5 - An automated server for topology generation
  Automated Topology builder – a newer server for topology generation
  OPLS-AA Topolbuild - Converts a Tripos .mol2 file into a topology
  TopolGen - Converts an all-atom .pdb file to a topology
  mktop - Converts a .pdb file into a topology
  TPPMKTOP -Have not tested…
  Also, have a look at STaGE (dx.doi.org/10.1021/jp505332p uses many different tools) and
  TopoGromacs (DOI: 10.1021/acs.jcim.6b00103 conversion tool between CHARMM and Gromacs)
  This tutorial is pretty cool and shows how to setup OPLS/aa topologies using some of the above tools/programs http://www.esi.umontreal.ca/~pelletjo/gromacs/derive09.html

## Slide 22
  How to setup the molecular topology for Gromacs
  i.e. the molecular topology file (.top or .itp, sort of flexible format)
  Caveat - Most topology utilites do not take into account bonds over the pbc’s 
  VMD’s inorganic builder + VMD plugin topotools? Can give you an .psf file
  Note, the atom matlab script can write a topology file for the inorganic builder!
  psf2top.py (github.com/resal81/PyTopol) can convert CHARMM .psf to .top/.itp files?
  psf2itp.py (Charmm-gui) can convert CHARMM .psf to .itp files?
  Gromacs topology tools/scripts for inorganic molecules/forcefields which can deal with pbc
  clayff_atom.m & write_atom_itp.m - generates a Clayff topologies
  interface_atom.m & write_atom_itp.m - generates an INTERFACE topologies
  I heard Materials studio is also great for this…

## Slide 23: 3/4 Example: Simulation of a small water box
500 SPC molecules with Gromacs 2016.3

## Slide 24: Example: Simulating water example input files… workflow 1
batch01 ; Optional. Needed to run on a HPC cluster in parallell
; hence we do not really need one for local jobs
job1.sh ; bash file executing the overall workflow (running gmx grompp/mdrun)
topol.top ; describes the system, and links the files below together
forcefield.itp ; describes some [ default ] parameters for the forcefield
ffnonbonded.itp ; holds the [ atomtypes ] and their nonbonded LJ parameters
ffbonded.itp ; holds the [ bond/angletypes ] and their bonded parameters
spc.itp ; holds the molecular topology of the spc water model
posres.itp ; special constraint settings
index.ndx ; file used to team up atoms/molecules/residues in groups. It is ; generated by the ’gmx make_ndx’ utility
Multiple simulations… multiple .mdp files
em.mdp ; energy minimization parameter file.
nvt.mdp ; N,V,T molecular dynamics parameter file
npt.mdp ; N,P,T molecular dynamics parameter file
md.mdp ; Production run molecular dynamics parameter file. Could be
; a N,V,T or a N,P,T or a N,V,E simulation…

## Slide 25
#include "forcefield.itp"
#include "spc.itp"
#include "posres.itp"
; System description
[ system ]
; Title of the system
Water with water with water...
[ molecules ]
;Compound number of molecules
SOL 500
Example: Simulating water The topol.top file… (see also section 5.8 in the Gromacs manual)

## Slide 26
  #define _FF_OPLS ; Means we want to use the ff files from the Gromacs distribution
  #define _FF_OPLSAA
; Default forcefield settings
[ defaults ]
; nbfunc comb-rule gen-pairs fudgeLJ fudgeQQ
1 2 no 1.0 1.0
#include "ffnonbonded.itp"
#include "ffbonded.itp”
nbfunc - is the non-bonded function type. Use 1 (Lennard-Jones) or 2 (Buckingham)
comb-rule - is the combination rule, for 1 & 3 see eq. 4.6, for 2 see eq. 4.7
gen-pairs - yes or no. If yes, used to generate pair interactions between 1,4 atoms not already defined in a [ pairtypes ] section. Important for certain forcefields and organic molecules
fudgeLJ - scaling factor to reduce the LJ (Lennard-Jones) interactions between 1,4 atoms
fudgeQQ - scaling factor to reduce the Coulomb interactions between 1,4 atoms
Example: Simulating water The forcefield.itp file…

## Slide 27
[ atomtypes ]
;name at.num mass charge ptype sigma epsilon
HW 1 1.00794 0.4100 A 0.000000 0.000000 ; Water hydrogen
OW 8 15.99940 -0.8200 A 0.316556 0.650170 ; Water oxygen
  The [ atomtypes ] section contains the specific ff’s non-bonded parameters for each atom type.
  It should contain the atom number, mass, charge, particle type, the LJ parameters sigma and epsilon (or C6 C12 if comb. rule 1, see previous slide).
Example: Simulating water The ff parameter files. Starting with the ffnonbonded.itp
Comb. rule 1 (& 3)
Comb. rule 2

## Slide 28
[ bondtypes ]
;i j func b0 kb
OW HW 1 0.1 463700
[ angletypes ]
;i j k func th0 cth
HW OW HW 1 109.47 383
  The [ bondtypes/angletypes ] sections contains the force-fields bonded parameters between all bonded atomtypes. See also the Gromacs manual, section 4.2 and 5.5.
Example: Simulating water The ff parameter files. The ffbonded.itp – hey, whats the units?

## Slide 29
Example: Simulating water The ff parameter files. The ffbonded.itp – Btw, whats the units?

## Slide 30
Example: Simulating water The ff parameter files. The ffbonded.itp – Btw, whats the units?

## Slide 31
Example: Simulating water Btw… what’s the units used in Gromacs? See Chp 2 in manual…
Gromacs manual 2016.3

## Slide 32
[ moleculetype ]
; molname nrexcl
SOL 2
[ atoms ]
; nr type resnr residue atom cgnr charge mass
#ifndef HEAVY_H
1 OW 1 SOL OW 1 -0.82 15.99940
2 HW 1 SOL HW1 1 0.41 1.00794
3 HW 1 SOL HW2 1 0.41 1.00794
#else
1 OW 1 SOL OW 1 -0.82 9.95140
2 HW 1 SOL HW1 1 0.41 4.03200
3 HW 1 SOL HW2 1 0.41 4.03200
#endif
#ifndef FLEXIBLE
[ settles ]
; OW funct doh dhh
1 1 0.1 0.16330
[ exclusions ]
1 2 3
2 1 3
3 1 2
#else
[ bonds ]
; i j funct length force.c.
1 2 1 0.1 463700 0.1 463700 ; 0.1 345000 ; ‘Bug’ #222 in orig .itp file
1 3 1 0.1 463700 0.1 463700 ; 0.1 345000 ; ‘Bug’ #222 in orig .itp file
[ angles ]
; i j k funct angle force.c.
2 1 3 1 109.47 383 109.47 383
#endif
Each molecule type needs an template topology file (.itp)
The water topologies are a bit special in Gromacs due to the different #if statements and the [ settles ] algorithm.
How to use flexible SPC? Add to the .mdp:
define = -DFLEXIBLE
Example: Simulating water The molecular topology file for SPC water, i.e. spc.itp

## Slide 33
#ifdef POSRES
[ position_restraints ]
;i funct fcx fcy fcz
1 1 1000 1000 1000 ; OW
2 1 1000 1000 1000 ; HW1
3 1 1000 1000 1000 ; HW2
#endif
Position restraints are used to restrain atoms around a fixed point in space, which can be useful for equilibration purposes.
The [ position_restraints ] file (or section) can be created with the gmx genrestr utility or written in matlab or manually…
To use it, use the –DPOSRES.itp flag in the corresponding .mdp file, this:
define = -DPOSRES
Example: Simulating water The position restraints file/s… posres.itp

## Slide 34
; System description
[ system ]
; Title of the system
Water with water with water...
[ molecules ]
;Compound number of molecules
SOL 500
The [ system ] section contains the actual system description for the current simulation. First it needs a title of course. Secondly it also contains the [ molecules ] section, which basically states which molecules, and how many of them, exist in the system. Note that the compound name must be the same as in the molecult topology file (here spc.itp). When more than one moleculetype/compound exist, the order of them must be matched in the initial structure file (a .gro or .pdb file).
Example: Simulating water Last section in the topology file topol.top

## Slide 35
In terminal:
gmx help commands
analyze Analyze data sets
check Check and compare files
convert-tpr Make a modifed run-input file
density Calculate the density of the system
distance Calculate distances between pairs of positions
dump Make binary files human readable
editconf Convert and manipulates structure files
energy Writes energies to xvg files and display averages
genion Generate monoatomic ions on energetically favorable positions
genrestr Generate position restraints or distance restraints for index groups
grompp Make a run input file
h2order Compute the orientation of water molecules
hbond Compute and analyze hydrogen bonds
help Print help information
hydorder Compute tetrahedrality parameters around a given atom
insert-molecules Insert molecules into existing vacancies
make_ndx Make index files
mdrun Perform a simulation, do a normal mode analysis or an energy minimization
msd Calculates mean square displacements
rdf Calculate radial distribution functions
sigeps Convert c6/12 or c6/cn combinations to and from sigma/epsilon
solvate Solvate a system
traj Plot x, v, f, box, temperature and rotational energy from trajectories
trjcat Concatenate trajectory files
trjconv Convert and manipulates trajectory files
trjorder Order molecules according to their distance to a group
tune_pme Time mdrun as a function of PME ranks to optimize settings
velacc Calculate velocity autocorrelation functions
view View a trajectory on an X-Windows terminal
wham Perform weighted histogram analysis after umbrella sampling
x2top Generate a primitive topology from coordinates
xpm2ps Convert XPM (XPixelMap) matrices to postscript or XPM
Example: Simulating water Some of the Gromacs 93 utilities/programs…

## Slide 36
  #!/bin/bash
  ## Create a simple water simulation box using the gmx solvate utility
  gmx solvate -cs spc216.gro -o preem.gro -p topol.top -maxsol 500 -box 2.5 2.5 2.5
  ## Make an index file with:
  echo q | gmx make_ndx -f preem.gro -o index.ndx
  ## Energy minimization
  gmx grompp -f em.mdp -c preem.gro -p topol.top -n index.ndx –pp em.top -o em.tpr -maxwarn 1
  gmx mdrun -v -deffnm em
  ## Short NVT simulation with fixed N, volume and T, and position restraints
  gmx grompp -f nvt.mdp -c em.gro -p topol.top -n index.ndx –pp nvt.top -o nvt.tpr gmx mdrun -v -deffnm nvt
  ## NPT simulation with fixed N, pressure and T, with no position restraints
  gmx grompp -f npt.mdp -c nvt.gro -p topol.top -n index.ndx –pp npt.top -o npt.tpr gmx mdrun -v -deffnm npt
  ## The actual production run
  gmx grompp -f md.mdp -c npt.gro -p topol.top -n index.ndx –pp md.top -o md.tpr gmx mdrun -v -deffnm md
  rm -f \#*
Example: Simulating water A typical bash job file (job1.sh)

## Slide 37
Example: Simulating water A typical bash job file (job1.sh)
  ; Here we create our actual system, a simulation box with 500 water molecules in a cubical box width length 2.5 nm. Gromacs does this by stacking a smaller box of 216 SPC water molecules and removing all water molecules that end up outside the box or overlap with other molecules.
  ; This command then results in a .gro file called preem.gro. Let’s have a look…
  ; Note! .gro files have a fixed format, and note there is no velocities here, since otherwise you would see three more columns after the x, y, z coordinates.
  Looking at preem.gro. Note the fixed format!
  Generated by gmx solvate.
  1500
  1SOL OW 1 0.230 0.628 0.113
  1SOL HW1 2 0.137 0.626 0.150
  1SOL HW2 3 0.231 0.589 0.021
  2SOL OW 4 0.225 0.275 0.996
  2SOL HW1 5 0.260 0.258 1.088
  2SOL HW2 6 0.137 0.230 0.984
  .
  .
  499SOL OW 1495 1.937 2.207 1.895
  499SOL HW1 1496 1.845 2.179 1.866
  499SOL HW2 1497 1.968 2.284 1.839
  500SOL OW 1498 1.934 2.028 2.180
  500SOL HW1 1499 1.917 2.111 2.126
  500SOL HW2 1500 2.024 1.991 2.158
  2.50000 2.50000 2.50000
  #!/bin/bash
  ## Create a simple water simulation box using the gmx solvate utility
  gmx solvate -cs spc216.gro -o preem.gro -p topol.top -maxsol 500 -box 2.5 2.5 2.5

## Slide 38
Example: Simulating water A typical bash job file (job1.sh)
  ; Here we create ’groups’ and prints the index of each atom belonging to certain groups to a text file (index.ndx) for housekeeping. The ’groups’ is a essential concept in Gromacs that allows us to treat or analyze groups of atoms separately. The utility gmx make_ndx allows us to select/create groups based upon atom and residue names or index number. For more comlicated selections, we could also use gmx select
  The echo q | is a bash command that lets us run gmx make_ndx automatically in the bash shell,
  Since it otherwise runs interactively. Output:
  Reading structure file
  Going to read 0 old index file(s)
  Analysing residue names:
  There are: 500 Water residues
  0 System : 1500 atoms
  1 Water : 1500 atoms
  2 SOL : 1500 atoms
  nr : group ! 'name' nr name 'splitch' nr Enter: list groups
  'a': atom & 'del' nr 'splitres' nr 'l': list residues
  't': atom type | 'keep' nr 'splitat' nr 'h': help
  'r': residue 'res' nr 'chain' char
  "name": group 'case': case sensitive 'q': save and quit
  'ri': residue index
  #!/bin/bash
  ## Create a simple water simulation box using the gmx solvate utility
  gmx solvate -cs spc216.gro -o preem.gro -p topol.top -maxsol 500 -box 2.5 2.5 2.5
  ## Make an index file with:
  echo q | gmx make_ndx -f preem.gro -o index.ndx

## Slide 39
Example: Simulating water A typical bash job file (job1.sh)
  ; Here we create ’groups’ and prints the index of each atom belonging to certain groups to a text file (index.ndx) for housekeeping. The ’groups’ is a essential concept in Gromacs that allows us to treat or analyze certain atoms/residues separately. The utility gmx make_ndx allows us to select/create groups based upon atom and residue names or index number. For more comlicated selections, we could also use gmx select.
  Another way of doing it is through this cat command:
  cat << EOF | gmx make_ndx -f preem.gro -o index.ndx
  a OW
  name 3 OW
  a HW*
  name 4 HW
  q
  EOF
  ; This allows us to create extra groups apart from the default groups
  ; Hence here we also created a (third) group called OW from all the OW ; atoms and a (fourth) group called HW from all the HW* atoms
  0 System : 1500 atoms
  1 Water : 1500 atoms
  2 SOL : 1500 atoms
  3 OW : 500 atoms
  4 HW : 1000 atoms
  #!/bin/bash
  ## Create a simple water simulation box using the gmx solvate utility
  gmx solvate -cs spc216.gro -o preem.gro -p topol.top -maxsol 500 -box 2.5 2.5 2.5
  ## Make an index file with:
  echo q | gmx make_ndx -f preem.gro -o index.ndx

## Slide 40
  We could optionally use the –maxwarn flag which allows gmx grompp to ignore potential problems/errors in the input files. With the flag –pp gmx grompp also outputs the final and explicit system topology file em.top. With –po the corresponding output em.mdp file is also printed (else mdout.mdp).
  ; Secondly, we run the actual simulation using gmx mdrun (on a hpc cluster this command can look a bit different, like gmx_seq_mdrun or gmx_mpi mdrun). The –v flag makes is verbose. The –deffnm defines the name of the input/output files, otherwise Gromacs uses its own default names.
  ; Then after the energy minimization, we proceed in a similar manner with the NVT,NPT and MD simulations.
Example: Simulating water A typical bash job file (job1.sh)
  #!/bin/bash
  ## Create a simple water simulation box using the gmx solvate utility
  gmx solvate -cs spc216.gro -o preem.gro -p topol.top -maxsol 500 -box 2.5 2.5 2.5
  ## Make an index file with:
  echo q | gmx make_ndx -f preem.gro -o index.ndx
  ## Energy minimization
  gmx grompp -f em.mdp -c preem.gro -p topol.top -n index.ndx –pp em.top -o em.tpr -maxwarn 1
  gmx mdrun -v -deffnm em

## Slide 41
  ; Parameters describing what to do, when to stop and what to save
  define = -DFLEXIBLE; Turn on flexible SPC water bonds
  integrator = steep ; Algorithm (steep = steepest descent minimization)
  emtol = 1000 ; Stop minimization when the maximum force < 1000.0 kJ/mol/nm
  emstep = 0.01 ; Energy step size
  nsteps = 1000 ; Maximum number of (minimization) steps to perform
  nstxout = 10 ; trajectory output every 10 steps
  cutoff-scheme = verlet
  ; Parameters describing how to find the neighbors of each atom and how to calculate the interactions
  nstlist = 10 ; Frequency to update the neighbor list and long range forces
  ns_type = grid ; Method to determine neighbor list (simple, grid)
  rlist = 1 ; Cut-off for making neighbor list (short range forces)
  coulombtype = PME ; Treatment of long range electrostatic interactions
  rcoulomb = 1 ; Short-range electrostatic cut-off
  rvdw = 1 ; Short-range Van der Waals cut-off
  pbc = xyz ; Periodic Boundary Conditions
Example: Simulating water A typical md parameter file for energy minization, em.mdp
With this input gmx grompp will produce a commented file with the default name mdout.mdp. That file will contain the above options, as well as all other options not explicitly set, showing their default values.
For all .mdp options, go to:
http://manual.gromacs.org/documentation/2016.3/user-guide/mdp-options.html

## Slide 42
  define = -DFLEXIBLE -DPOSRES
  ; Run parameters
  Integrator = md ; leap-frog integrator
  nsteps = 10000 ;
  nstcomm = 1000 ;
  dt = 0.0005 ; 0.5 fs
  comm-mode = Linear ; Linear COM mass control every 1000 steps
  comm-grps = SYSTEM ; Groups to apply COM control to
  ; Output control
  nstxout = 0 ; every 0 ps
  nstvout = 0 ; save velocities every 0 ps
  nstfout = 0 ; save forces every 0 ps
  nstxout-compressed = 100 ; xtc compressed trajectory output every 0.5 ps
  nstenergy = 100 ; save energies every 0.5 ps
  nstlog = 100 ; update log file every 0.5 ps
  ; Bond parameters
  continuation = no ; first dynamics run
  constraint_algorithm = lincs ; holonomic constraints
  constraints = none ; all bonds (even heavy atom-H bonds) constrained
  lincs_iter = 1 ; accuracy of LINCS
  lincs_order = 4 ; also related to accuracy
  ;see more on next slide…
  ; A word about bonds or constraints as we call it in Gromacs – To constrain the bonds, we could use shake as the constraint_algorithm but lincs is preferable since its more stable and faster (I think). Note that even if we set constraints = none ; the water (as set in the water .itp file) still will have its bonds and angles constrained by the settle algorithm, unless we have set define = -DFLEXIBLE
Example: Simulating water A typical md parameter file for a NVT simulation, nvt.mdp

## Slide 43
  ;cont’d from previous slide
  ; Neighborsearching
  cutoff-scheme = verlet
  ns_type = grid ; search neighboring grid cells
  nstlist = 10 ; 10 fs
  rlist = 1.0 ; short-range neighborlist cutoff (in nm)
  ; Electrostatics and vdw
  coulombtype = PME ; Particle Mesh Ewald for long-range electrostatics
  pme_order = 4 ; cubic interpolation
  fourierspacing = 0.16 ; grid spacing for FFT
  rcoulomb = 1.0 ; short-range electrostatic cutoff (in nm)
  rvdw = 1.0 ; short-range van der Waals cutoff (in nm)
  ; Temperature coupling is on
  tcoupl = V-rescale ; modified Berendsen thermostat
  tc-grps = SYSTEM ; on coupling groups - more accurate
  tau_t = 0.1 ; time constant, in ps
  ref_t = 298.15 ; reference temperature, one for each group, in K
  ; Pressure coupling is off
  pcoupl = no ; no pressure coupling in NVT
  ; Periodic boundary conditions
  pbc = xyz ; 3-D PBC
  periodic-molecules = no
  ; Dispersion correction
  DispCorr = EnerPres ; account for cut-off vdW scheme
Example: Simulating water A typical md parameter file for a NVT simulation, nvt.mdp

## Slide 44
  ; Temperature coupling is on
  tcoupl = V-rescale ; modified Berendsen thermostat
  tc-grps = SYSTEM ; on coupling groups - more accurate
  tau_t = 0.1 ; time constant, in ps
  ref_t = 298.15 ; reference temperature, one for each group, in K
Example: Simulating water A typical md parameter file for a NVT simulation, nvt.mdp
  ; A word about thermostats –
  tcoupl -Several groups can be coupled separately, these are specified in the tc-grps field separated by spaces.
no - No temperature coupling
berendsen - Temperature coupling with a Berendsen-thermostat to a bath with temperature ref-t [K], with time constant tau-t [ps]
nose-hoover - Temperature coupling using a Nose-Hoover extended ensemble. The reference temperature and coupling groups are selected as above, but in this case tau-t [ps] controls the period of the temperature fluctuations at equilibrium
v-rescale - Temperature coupling using velocity rescaling with a stochastic term (JCP 126, 014101). This thermostat is similar to Berendsen coupling, with the same scaling using tau-t, but the stochastic term ensures that a proper canonical ensemble is generated. The random seed is set with ld-seed. This thermostat works correctly even for tau-t=0. For NVT simulations the conserved energy quantity is written to the energy and log file.

## Slide 45
  ;In nvt.mdp
  ; Pressure coupling is off
  Pcoupl = no ; no pressure coupling in NVT
  ;In npt.mdp
  ; Pressure coupling is on
  pcoupl = Berendsen ; Parrinello-Rahman ; Pressure coupling on in NPT
  pcoupltype = isotropic ; uniform scaling of box vectors
  tau-p = 5 ; time constant, in ps
  ref-p = 1.0 ; reference pressure, in bar
  compressibility = 4.5E-5 ; isothermal compressibility of water, bar^-1
  ; also, set
  continuation = yes ; because the second dynamics run
Example: Simulating water A typical md parameter file for a NVT simulation, nvt.mdp
  ; A word about barostats – pcoupl
  no - No pressure coupling. This means a fixed box size.
  Berendsen - Exponential relaxation pressure coupling with time constant tau-p [ps]. The box is scaled every timestep. It has been argued that this does not yield a correct thermodynamic ensemble, but it is the most efficient way to scale a box at the beginning of a run.
  Parrinello-Rahman - Extended-ensemble pressure coupling where the box vectors are subject to an equation of motion.
  pcoupltype = Isotropic | semiisotropic | anisotropic | surface-tension

## Slide 46
Example: Simulating water A typical bash job file (job1.sh)
  #!/bin/bash
  ## Create a simple water simulation box using the gmx solvate utility
  gmx solvate -cs spc216.gro -o preem.gro -p topol.top -maxsol 500 -box 2.5 2.5 2.5
  ## Make an index file with:
  echo q | gmx make_ndx -f preem.gro -o index.ndx
  ## Energy minimization
  gmx grompp -f em.mdp -c preem.gro -p topol.top -n index.ndx –pp em.top -o em.tpr -maxwarn 1
  gmx mdrun -v -deffnm em
  ## Short NVT simulation with fixed N, volume and T, and position restraints
  gmx grompp -f nvt.mdp -c em.gro -p topol.top -n index.ndx –pp nvt.top -o nvt.tpr gmx mdrun -v -deffnm nvt
  ## NPT simulation with fixed N, pressure and T, with no position restraints
  gmx grompp -f npt.mdp -c nvt.gro -p topol.top -n index.ndx –pp npt.top -o npt.tpr gmx mdrun -v -deffnm npt
  ## The actual production run
  gmx grompp -f md.mdp -c npt.gro -p topol.top -n index.ndx –pp md.top -o md.tpr gmx mdrun -v -deffnm md
  rm -f \#*

## Slide 47
Before
After
Easily becomes too many files in a single folder!! Especially for more advanced workflows..
Can we simplify this somehow?
Example: Simulating water The input files before and after the simulations… workflow 1

## Slide 48
Before
After
Example: Simulating water The input files before and after the simulations… workflow 2
using some bash scripting
We should make use of bash to create rational workflows! Why?
It can make things tidy
Allows us to create advanced workflows
Allows us to run same input files on different computers/HPC clusters

## Slide 49
  #!/bin/bash
  cluster=$1 # Passed variable 1 (machine) from caller
  ncores=$2 # Passed variable 2 (number of proc.) from caller
  ## SET MAIN DIRECTORY TO CURRENT PATH ############################
  gmx_run=$(pwd)
  echo "home directory of the gromacs simulations set to $gmx_run"
  ## SET TWO MOLECULE/FILENAME KEYWORDS ############################
  I=SOL
  J=gmx
  moldir="$I"_"$J"
  ## Let’s define some variable just for fun that we could in the simulations
  Temp=298.15
  ## CREATE THE SYSTEM AND A INDEX FILE ############################
  ## Create a simple water simulation box using the gmx solvate utility
  gmx solvate -cs spc216.gro -o $moldir/preem.gro -p $moldir/topol.top -maxsol 500 -box 2.5 2.5 2.5
  ## Make an index file with:
  echo q | gmx make_ndx -f $moldir/preem.gro -o $moldir/index.ndx
  ## RUN THE RUN SCRIPTS ###########################################
  source ./run_0_set_machine.sh $cluster $ncores
  source ./run_1_em.sh 1000 10
  source ./run_2_nvt.sh 10000 1000
  source ./run_3_npt.sh 10000 1000
  source ./run_4_md.sh 1000000 1000
Note that all the .mdp files are inside the bash run scripts along with the gmx grompp and gmx mdrun commands!
Example: Simulating water The alternative job file job1.sh file, using bash scripting… workflow 2

## Slide 50
  #!/bin/bash
  cluster=$1 # Passed variable 1 (machine) from caller
  ncores=$2 # Passed variable 2 (number of proc.) from caller
  if [[ $# -eq 0 ]]; then
  echo "no passed variables"
  else
  nPME=$((${ncores}/4)) # Number of dedicated PME cores
  fi
  if [[ $cluster == "beskow" ]] # This now seems to be for gromacs 5.1.2.
  then
  echo "Cluster is beskow"
  echo "will run on $ncores proc.”
  export OMP_NUM_THREADS=1
  ## APRUN_OPTIONS="-n ${ncores} -d 1 -cc none"
  gmx_mdrun="aprun -n ${ncores} -d 1 -cc none gmx_mpi mdrun -npme ${nPME}"
  gmx_grompp="gmx_seq grompp"
  gmx_wham="gmx_seq wham"
  gmx_dist="gmx_seq distance”
  elif [ $cluster = "abisko" ] # This now seems to be for gromacs 5.1.1.
  then
  echo "Cluster is abisko"
  echo "will run on $ncores proc."
  # For Abisko only!
  if [ -n "$SLURM_CPUS_PER_TASK" ]; then
  md="mdrun_mpi -ntomp $SLURM_CPUS_PER_TASK -npme ${nPME}"
  else
  md="mdrun_mpi -ntomp 1"
  fi
  gmx_mdrun="srun $md”
  gmx_grompp="gmx grompp”
  gmx_wham="gmx wham”
  gmx_dist="gmx distance"
  fi
Note that different HPC centers and local computers might use different gmx run commands!
Making use of some bash if-statements!
Example: Simulating water Set computer specific settings in a separate file (run_0_set_machine.sh) This file makes the input files compatible with different computers

## Slide 51
  # Cont’d from previous slide
  else
  echo "no cluster, running on local machine"
  echo "will run on $ncores proc."
  # Do we want to run with a specific Gromacs version
  # source /usr/local/gromacs-5.1.1/bin/GMXRC
  # source /usr/local/gromacs-5.1.4/bin/GMXRC
  # source /usr/local/gromacs-2016.3/bin/GMXRC
  gmx_mdrun="gmx mdrun"
  gmx_grompp="gmx grompp"
  gmx_wham="gmx wham"
  gmx_dist=”gmx distance”
  fi
  echo $run_cmd
  echo $run_grompp
No $cluster of $ncores variables needs to be defined when running on our own local computer, hence we finish the if-statement with an else…
Example: Simulating water Set computer specific settings in a separate file (run_0_set_machine.sh) This file makes the input files compatible with different computers

## Slide 52
  #!/bin/bash
  sim=em
  type=EM
  ## Set main directory to current path
  gmx_run=$(pwd)
  echo "home directory of the gromacs simulations set to $gmx_run"
  if [ $# -eq 0 ]
  then
  echo "No n steps supplied"
  nsteps=1000
  else
  nsteps=$1
  fi
  if [ $# -lt 2 ]
  then
  echo "No n steps supplied"
  emtol=1000
  else
  emtol=$1
  fi
  if [ $# -lt 3 ]
  then
  echo "No framerate supplied"
  framerate=10
  else
  framerate=$2
  fi
  echo "Starting energy minimization steep"
  cd $gmx_run
  mkdir "$type”
  cd "$type”
  cp $gmx_run/$moldir/preem.gro ./pre"$sim".gro
If no $nsteps or $framerate variables are defined, we should use some default values
Example: Simulating water A first run file - run_1_em.sh

## Slide 53
  ################################################
  ####### ENERGY MINIMIZATION WITH STEEP #########
  ################################################
  ### Create em.mdp file ########################################
  cat << EOF >| "$sim".mdp
  ; Parameters describing what to do, when to stop and what to save
  define = -DFLEXIBLE ; position restrain the protein
  integrator = steep ; Algorithm (steep = steepest descent minimization)
  emtol = $emtol ; Stop minimization when the maximum force < 1000.0 kJ/mol/nm
  emstep = 0.01 ; Energy step size
  nsteps = $nsteps ; Maximum number of (minimization) steps to perform
  Nstxout = $framerate ; xtc compressed trajectory output every .1 ps
  cutoff-scheme = verlet
  ; Parameters describing how to find the neighbors of each atom and how to calculate the interactions
  Nstlist = 10 ; Frequency to update the neighbor list and long range forces
  ns_type = grid ; Method to determine neighbor list (simple, grid)
  rlist = 1 ; Cut-off for making neighbor list (short range forces)
  coulombtype = PME ; Treatment of long range electrostatic interactions
  rcoulomb = 1 ; Short-range electrostatic cut-off
  rvdw = 1 ; Short-range Van der Waals cut-off
  pbc = xyz ; Periodic Boundary Conditions
  periodic-molecules = yes
  EOF
  ################################################
  ####### ENERGY MINIMIZATION WITH STEEP #########
  ################################################
  $run_grompp -f ./"$sim".mdp -c pre"$sim".gro -p $gmx_run/$moldir/topol.top -n $gmx_run/$moldir/index.ndx -o "$sim".tpr -maxwarn 1
  $run_cmd -v -deffnm "$sim”
  echo "Minimization steep complete."
  if [ -e "$sim".gro ]
  then
  echo "Minimization steep may have finished ok!"
  cp "$sim".gro ../
  fi
  cd $gmx_run
We use cat << EOF >| to print the .mdp file and to run gmx grompp and gmx mdrun. After finished, cd to the working folder
Example: Simulating water A first run file - run_1_em.sh

## Slide 54
  ################################################
  ########### VOLUME EQUILIBRATION ##############
  ################################################
  echo "Starting "$type" simulation"
  cd $gmx_run
  latest_gro=$(ls -t1 *.gro | head -n1)
  echo $latest_gro
  mkdir "$type"
  cp $latest_gro ./"$type"/pre"$sim".gro
  cd "$type"
  The subsequent NVT, NPT and MD simulations work the same way, except now the most recent .gro file from the working folder is copied to the current simulation folder (instead of the $moldir/preem.gro) and used as the input structure. This has some different advantages but also some disadvantages… can you see why?
Example: Simulating water The subsequent NVT, NPT snd MD simulation files…

## Slide 55
  What’s in a .log text file? Best reference can be found here:
  http://www.gromacs.org/Documentation/Tutorials/GROMACS_USA_Workshop_and_Conference_2013
  What’s in a .edr file? Use gmx energy to find out, like this
  prenpt.gro # The input structure, hence the ’pre’
  npt.gro # The final structure, what if we can’t find it?
  npt.xtc # The compressed trajectory, why not .trr?
  npt.tpr # The input .tpr file created by gmx grompp
  npt.log # The simulation log file. How did we do?
  npt.edr # The output energy file. Use with gmx energy npt.mdp # Our md parameter file
  mdout.mdp # Gromacs md parameter file, Wait, what? (-po)
  npt.top # Gromacs topology file. Wait, what? (-pp)
  npt.cpt # The restart checkpoint file.
Let’s have a look at some output files
Example from the NPT simulations
  gmx energy –f npt.edr
  echo 5 10 11 | gmx energy –f npt.edr

## Slide 56
  Opened npt.edr as single precision energy file
  Select the terms you want from the following list by
  selecting either (part of) the name or the number or a combination.
  End your selection with an empty line or a zero.
  -------------------------------------------------------------------
  1 LJ-(SR) 2 Disper.-corr. 3 Coulomb-(SR) 4 Coul.-recip.
  5 Potential 6 Kinetic-En. 7 Total-Energy 8 Temperature
  9 Pres.-DC 10 Pressure 11 Box-X 12 Box-Y
  13 Box-Z 14 Volume 15 Density 16 pV
  17 Enthalpy 18 Vir-XX 19 Vir-XY 20 Vir-XZ
  21 Vir-YX 22 Vir-YY 23 Vir-YZ 24 Vir-ZX
  25 Vir-ZY 26 Vir-ZZ 27 Pres-XX 28 Pres-XY
  29 Pres-XZ 30 Pres-YX 31 Pres-YY 32 Pres-YZ
  33 Pres-ZX 34 Pres-ZY 35 Pres-ZZ 36 #Surf*SurfTen
  37 T-System 38 Lamb-System
  5
  10
  11
  Back Off! I just backed up energy.xvg to ./#energy.xvg.1#
  Last energy frame read 1000 time 100.000
  Statistics over 100001 steps [ 0.0000 through 100.0000 ps ], 3 data sets
  All statistics are over 1001 points (frames)
  Energy Average Err.Est. RMSD Tot-Drift
  -------------------------------------------------------------------------------
  Potential -20866 17 140.671 -56.7338 (kJ/mol)
  Pressure -23.6986 21 520.216 114.21 (bar)
  Box-X 2.48375 0.0011 0.00363595 -0.00628363 (nm)
  gcq#27: "A Man Needs a Maid" (N. Young)
  If we did not use the –o flag, gmx energy will output energy.xvg as default. Now we could take a look at it using xmgrace by using this command (or the import_xvg(‘energy.xvg’) matlab function)
  xmgrace –nxy energy.xvg
Let’s have a look at some output files
Example from the NPT simulations
  gmx energy –f npt.edr
  echo 5 10 11 | gmx energy –f npt.edr
  gmx energy -f ener.edr << EOF
  Pot
  Kin
  Tot
  EOF
…or try 

## Slide 57
  xmgrace –nxy energy.xvg
  ; Has the system equilibrated? Look at Potential energy, pressure, box size…
  ; Hey, what does the –nxy flag do?
Let’s have a look at some output files
Example from the NPT simulations

## Slide 58
  #!/bin/bash
  # bash script to analyze the density of the system
  type=MD
  sim=md
  cd $type
  echo 0 | gmx density -f $sim.xtc -s $sim.tpr -o density.xvg \
  -d z -sl 200
  gmx analyze -f density.xvg -errbar stddev -aver_start 100
  rm -f \#*
  xmgrace -nxy density.xvg &
  cd ..
Some simple trajectory analysis
Example with the MD run simulations, assuming files exist in a subfolder called MD

## Slide 59
  #!/bin/bash
  # bash script to analyze the mean-square-displacement and the diffusion # coefficient of the molecules
  type=MD
  sim=md
  cd $type
  echo 0 | gmx msd -f md.xtc -s md.tpr -o msd.xvg -trestart 250 -beginfit 20 -endfit 250
  xmgrace -nxy msd.xvg &
Some simple trajectory analysis
Example with the MD run simulations, assuming files exist in a subfolder called MD

## Slide 60
  #!/bin/bash
  # bash script to analyze the hydrogen bonds in the system
  type=MD
  sim=md
  cd $type
  echo 0 0 | gmx hbond -f $sim.xtc -s $sim.tpr -n ../SOL_gmx/index.ndx -temp 298 -num hbnum.xvg -hbn hbond.ndx -nhbdist nhbdist.xvg -g hbond.log -dist hbdist.xvg -ang hbang.xvg
  gmx analyze -f hbnum.xvg
  xmgrace -nxy hbnum.xvg &
  rm -f \#*
Some simple trajectory analysis
Example with the MD run simulations, assuming files exist in a subfolder called MD

## Slide 61
  #!/bin/bash
  # bash script to analyze the radial distribution function between OW – HW
  # in blocks using a for loop
  type=MD
  sim=md
  cd $type
  block=200
  for N in 1 2 3 4 5;
  do (start=$(($N*$block-$block))
  stop=$(($N*$block))
  echo $start
  echo $stop
  echo 2 2 | gmx rdf -f $sim.xtc -s $sim.tpr -n ../SOL_gmx/index.ndx \
  -ref OW -sel HW -bin 0.002 -rmax 1.2 -o rdf_OwHw_$N.xvg \
  -cn rdf_OwHw_cn_$N.xvg -b $start -e $stop
  );
  done
  rm -f \#*
  xmgrace -nxy rdf_*.xvg &
  cd ..
Radial distribution
Some simple trajectory analysis
Example with the MD run simulations, assuming files exist in a subfolder called MD using a for-loop to look at time dependency

## Slide 62: The End